PRODUCTS SPECIFICATION

FLLED30MP 30W LED Floodlight

(110V 30W minipod LED light)

【Datasheet 】

| Type | Product | LED FloodLight |
| --- | --- | --- |
|  | Modle No | FLLED30MP |
|  | Product Type | outdoor Lighting |
|  | Safety Level | Class I |
|  | IP Level | IP44 |
|  | Safety Certificates | CE |
|  | RoHS Directive | Compliant |
| Electronical | Input Voltage | 110 AC |
|  | Frequency | 50/60Hz |
|  | Power | 30Watt |
|  | Power factor( PF) | ＞90％ |
|  | Total Harmonic Distortion | ＜20％ |
| Optical | Cover Material | Tempered glass lens |
|  | The whole lamp light Angle | 120° |
|  | LED Quantity | 1 |
|  | LED Package | COB |
|  | Luminous Efficiency(Lm/W) | ≥80Lm/W |
|  | LED luminous | Warm white | 2559LM |
|  |  | Pure white | 2860LM |
|  |  | Cold white | 2790LM |
|  | Color temperature(CCT) | Warm white | 2700-3500K |
|  |  | Pure white | 5500-6500K |
|  |  | Cold white | 7000-10000K |
|  | Color Render Index(CRI) | W W | Ra＞78 |
|  |  | C P W | Ra＞85 |
|  | Illuminance uniformity | ＞0.6 |
|  | Light distribution | Symmetric/rectangular flare |
|  | Light design | LED + reflectors secondary light distribution |
| Lamp Structure | Housing Material | Die-casting Aluminum body, powder coating |
| Others | Application | Outdoor or indoor |
|  | LED Junction temperature | ≤60℃ |
|  | Ambient Humidity | 10％~90％R.H. |
|  | Ambient Temperature | -25℃- 55℃ |
|  | Storage Tempertature | -30℃- 75℃ |
|  | Housing Tempertature（Working） | ＜60℃（Ta=25℃） |
|  | Lifespan | 50000H |
|  | Color of lamp shell | Yellow, black |
| Dimension | Power line | 3G1.5mm2 3mtr cable |
|  | Connect wire | Brown | L |
|  |  | Blue | N |
|  |  | Yellow/Green | E |
| Carton Box Dimension | Quantity of each Carton | 5PCS |
|  | Net Weight | 13.8kg |
|  | Gross Weight | 16kg |
|  | Inner Box Dimension | 28X14X30.5cm |
|  | Outer Box Dimension | 72x30x33cm |

【Light Distribution】

# Text boxes

Product name:          LED FloodLight

Item No     :              FLLED30MP

Power			:              30Watt

LED        :        1 pc COB x 30Watt

Input Voltage:           AC 110Voltage